## Slide 1: Creating a BLE112 Project

## Slide 2: BLE112 Projects – Where to start?
What is a project?
  A project is a collection of files together will define the BLE112’s functionality for a given application
What is the structure of a BLE112 project?
  A main project file is an XML file with references to associated files
  An example project file is as follows:
  <project>
  <gatt in=“gatt.xml” />
  <hardware in=“hardware.xml” />
  <script in=“bgdemo.bgs” />
  <usb_main in=“cdc.xml” />
  <image out=“out.hex” />
  </project>
Notes: The project configuration is described within the <project> tags
<gatt> tag defines the .XML file containing the GATT data base description (REQUIRED)
<hardware> tag defines the .XML file containing the hardware configuration (REQUIRED)
<script> tag defines the .BGS file containing the BGScript code.
  If the project does not contain a BGScript code, this tag can be simply left out.
<usb_main> tag defines the .XML file containing the USB descriptors description.
  If the project does not use USB interface, this tag can be simply left out.
<image> tag defines the output .HEX file containing the firmware image (REQUIRED)

## Slide 3: What goes into the gatt.xml file?
The gatt.xml file describes Bluetooth low energy profiles, services, their characteristics, and access rights
The function of gatt.xml is to expose the data to be communicated
  gatt.xml must include at least one SERVICE
  SERVICES require at least one CHARACTERISTIC
  SERVICES and CHARACTERISTICS each have UUID’s (universally unique identifier)
  PROPERTIES define how the CHARACTERISTIC can be accessed by a remote device
  VALUE defines the type and size of the data stored there
Developers can use Bluegiga’s Profile Toolkit Developer Guide and reference examples in the BLE112 SDK to help create specific gatt.xml implementations for their applications
Notes: Every Bluetooth low energy device needs to implement a GAP service.
    A list of the standard Bluetooth low energy UUIDs can be found on the Bluetooth.org website
    More details on implementing a GATT.XML are found in the Profile toolkit users guide.

## Slide 4: Options on transmitting/receiving data over BLE
Within the Characteristic PROPERTIES, values can be set to the following:
  READ
    value can be read over a BLE connection
  CONST
    value is stored in flash memory and it cannot be modified after programming
  WRITE
    value can be written over BLE connection
  WRITE NO RESPONSE
    value can be written only using a write_no_response command, meaining the write operation is not confirmed over the BLE connection.
  NOTIFY
    Value can be notified. Notification is not confirmed
  INDICATE
    Value can be indicated. Indication is confirmed
  AUTHENTICATED READ
    Reading the characteristic value over a BLE connection requires authentication. The READ ATRIBUTE must also be set to true
  AUTHENTICATED WRITE
    Writing characteristic value over a Bluetooth _connection requires authentication. WRITE or WRITE NO RESPONSE attribute must also be set to true.
Notes: Every Bluetooth low energy device needs to implement a GAP service.
    A list of the standard Bluetooth low energy UUIDs can be found on the Bluetooth.org website
    More details on implementing a GATT.XML are found in the Profile toolkit users guide.

## Slide 5: Example gatt.xml File
Notes: NOTE: If advertise="true" is not set in the service, the iPhone4S may not be able to discover the device.

## Slide 6: BGScript Project Structure
project.xml
hardware.xml
gatt.xml
  Database structure
  Security settings
glucose.bgs
  Main application logic
  Event detection
  I/O detection, display updates, sensor reading

## Slide 7: BGScript Projects
Allows for on-module applications, eliminating the need for an external host controller
  BGScript is similar to BASIC
  Code can be developed using an text or source code editor
  Code is executed in response to event messages
  Lines are executed in order
  Events need to be defined and finished with an end statement
Notes: Details of implementing BGSCripts programs can be found in BGScript users guide. Examples are available in SDK.

## Slide 8: BGScript Architecture
Notes: Details of implementing BGSCripts programs can be found in BGScript users guide. Examples are available in SDK.

## Slide 9: Hardware setup for BGScript Project
Enable BGScript (not BGAPI)
Enable low-power sleep modes
Enable UART if desired (e.g. debug data, external comms)
Enable SPI if desired (e.g. onboard display output)
Enable PORT 0 pull-down

## Slide 10: BGAPI Projects
BGAPI is binary API for use in applications where external host processor is needed.
  Binary commands are issued over UART or USB to BLE112 module
  Binary commands compiled into C library (BGLIB)
    BGLIB can be recompiled for specific host platforms
    Example – Arduino implementation
  Example Binary API projects contained with SDK
  BGScript examples can be used as reference for BGAPI applications
Notes: Details of implementing BGSCripts programs can be found in BGScript users guide. Examples are available in SDK.

## Slide 11: BGAPI Architecture
Notes: Details of implementing BGSCripts programs can be found in BGScript users guide. Examples are available in SDK.

## Slide 12: Hardware setup for BGAPI Project
Configure BGAPI on UART or USB
Other settings generally the same as BGScript project

## Slide 13: Glucose Project Example

## Slide 14: Glucose Project Structure
  <project>
  <gatt in=“gatt.xml” />
  <hardware in=“hardware.xml” />
  <script in=“glucose.bgs” />
  <usb_main in=“cdc.xml” />
  <image out=“out.hex” />
  </project>

## Slide 15: Glucose Hardware.XML Structure
  <hardware>
  <sleeposc enable="true" ppm="30" />
  <usb enable="false" />
  <txpower power="15" bias="5" />
  <script enable="true" />
  <slow_clock enable="false" />
  <pmux regulator_pin="7" />
  <usart channel="0" mode="spi_master" alternate="2" polarity="positive“
  phase="1" endianness="msb" baud="57600" endpoint="none" />
  <usart channel="1" alternate="1" baud="115200" endpoint="none“
  flow="false" />
  <port index="0" pull="down" />
  </hardware>

## Slide 16: Glucose Profile GATT Structure
Generic Access Service
  Device Name and Appearance
Glucose Service
  Glucose Measurement
  Glucose Measurement Context (optional)
  Glucose Feature
  Record Access Control Point
Device Information Service
  Manufacturer Name
  Model Number
  System ID

## Slide 17: Glucose Profile GATT Structure

## Slide 18: BGScript Event Code Overview
System Boot – on startup
Connection Status – connect/disconnect
Attribute Write – remote updates from iOS
Hardware I/O Status – button presses
Hardware Timer – background updates
ADC Result – data read from ADC

## Slide 19: Compiling and installing the project onto a BLE112
Recommended Approach
  USE BLE Update tool found on Bluegiga’s Tech Forum
  Connect CC Debugger to module
  Press button on CC Debugger and make sure LED turns green
  Start BLE Update Tool
    Make sure CC Debugger is shown in port dropdown list
  Browse to find your project
  Press update
Notes:   TI Flash tool should NOT be used with the Bluegiga Bluetooth Smart SDK v.1.1 or newer, but BLE Update tool should be used instead. The BLE112 and BLED112 devices contain a security key, which is needed for the firmware to operate and if the device is programmed with TI flash tool, this security key will be erased.

## Slide 20: Glucose Demo Usage
Advertising enabled after power-on
Connection with bonding enabled
Current status always displayed on LCD
Potentiometer: Set glucose measurement
P0_0 button: Initiate glucose reading
P0_1 button: Reset all saved data/bonding
iOS first/last/all record retrieval from flash

## Slide 21: Thank you!